## Slide 1: Commercial Data Processing Workflow
20250107

## Slide 2: Purpose & Context
Current Commercial Data Processing Workflow Understanding, Transition Needs, and Automation in Parallel
Purpose
  Restate Kal’s current commercial data process
  Confirm shared understanding of the workflow and assumptions
  Identify what is needed to transition ownership
  Clarify

## Slide 3: End-to-End Workflow
High-Level Process
  Data receipt via secure transfer
  Download, unpacking, and folder setup
  Manual organization and verification
  MRI handling
  TDC handling
  Treatment tracking
  SQLite (local.db) review
  PEDA execution
  Post-PEDA cleanup
  Upload, vaulting, and notification

## Slide 4: Data Preparation (MRI + TDC)
Data Intake & Setup
  Files downloaded from PMI secure email link
  Processed on RDC Toronto CPU
  Script creates folder structure and unpacks ZIPs
MRI Handling
  MRI ZIP unpacked and re-zipped
  No file renaming or modification
  De-identification with spot checks
TDC Handling
  TDC ZIP unpacked and reorganized
  Logs moved to expected locations
  Session folders re-zipped
  Raw folders removed after compression

## Slide 5: Review, PEDA, and Closeout
Structured Review
  local.db opened manually
  Patient-related fields checked
  Identifiers removed if present
PEDA Execution
  PEDA run via batch file
  Progress monitored
  Failures noted as needed
  Limited concurrency to manage resources, i.e., not parallelized (trivial parallelization), yet.
Post-PEDA
  Outputs separated (full data vs video)
  Large files stripped from video outputs
  Final artifacts zipped, uploaded, vaulted (sync.com via browser only)
  Standard notification sent

## Slide 6: What I’d Need to Take This Over
Transition
  Questions
    Who decides whether a step is required versus historical?
    Who decides whether specific fields (e.g., birth year) are preserved or removed?
    For questions beyond code execution—such as missing data handling or PHI edge cases—who is the authoritative point of contact?
    What is the governing SOP for these decisions and this process?
      Does one exist today?
      If not, is the expectation that I draft it? (I’m comfortable doing so.)
    When judgment calls are required, who absorbs the risk?
    How are decisions documented and defended later, e.g., during audits or reviews?
  Defined scope and expectations
  Access to equivalent processing environment
  A concrete transition plan with a handoff point
    I would like Kal to video record his screen for a GE, Siemens, and Philips case
    No need to narrate, just screen record and I’ll dig through it

## Slide 7: Automation in Parallel
Parallel Automation Strategy
  Replicate current assumptions first
  Validate automated outputs against existing results
  Run side-by-side until equivalence is confirmed
  Make changes incrementally
  Preserve current endpoints throughout
Goal Reduce manual risk over time without disrupting a working process
Risk-> typos, PHI misses, data loss, etc.

## Slide 8: Purpose of This Walkthrough
Restate current commercial data processing workflow as implemented today
Confirm shared understanding of the process and assumptions
Identify what is needed to transition ownership
Clarify how automation will proceed in parallel without disrupting output

## Slide 9: High-Level Workflow Overview
Data receipt (secure transfer)
Initial download and folder setup
Manual organization and verification
MRI handling
TDC handling
Treatment tracking
SQLite (local.db) review
PEDA execution
Post-PEDA cleanup
Upload, vaulting, and notification
Single-operator, serial process optimized for correctness and consistency

## Slide 10: Data Receipt & Setup
Data Intake
Files received via PMI secure transfer
Downloaded from email link
Processing performed on a dedicated high-resource machine via remote desktop
Initial Setup
Files downloaded to local Downloads
Script:
  prompts for site and treatment
  creates folder structure
  copies ZIPs
  unzips contents
Original ZIPs deleted after extraction

## Slide 11: Manual Organization & MRI Handling
Manual Organization
Data moved into standard folders:
  MRI
  TDC
  Treatment report
Treatment PDF opened to confirm no PHI, then closed
MRI Handling
  MRI ZIP unpacked
  ZIP deleted after extraction
  No renaming or modification unless required
  Relies on site-level de-identification
  Spot checks performed as needed

## Slide 12: TDC Handling & Tracking
TDC Handling
  TDC ZIP unpacked and deleted
  Folders renamed or reorganized for consistency
  Log folders moved to expected locations
  Session folders re-zipped
  Raw folders deleted after compression
Treatment Tracking
  Tracker updated manually:
    site ID
    treatment number
    upload date
    study designation
  Treatment marked “in processing”

## Slide 13: SQLite Review & PEDA Execution
SQLite (local.db) Review
  Database opened manually
  Patient-related fields checked
  Any identifiers removed if present
  Database closed after verification
Running PEDA
  PEDA launched via batch file (“Run PEDA”)
  No direct MATLAB interaction
  Progress monitored intermittently
  Failures retried as needed
  Concurrency kept low to manage resources

## Slide 14: Post-PEDA & Closeout
Post-PEDA Cleanup
  DICOM data zipped, raw folders removed
  PEDA outputs separated:
    full data
    video-only outputs
  .mat files stripped from video outputs
  Final artifacts zipped
Upload & Notification
  All ZIPs uploaded to Sync
  Data moved to vault locations
  Standard notification email sent
  Treatment marked complete
  TDC logs copied to Data Scientist NAS

## Slide 15: Key Characteristics of the Current Process
What Makes This Work Today
  Single accountable operator
  Well-established assumptions
  Manual verification where needed
  Outcome-focused, not tool-focused
  Optimized for correctness over scale

## Slide 16: What I’d Need to Take This Over
To Transition Ownership Successfully
  Clear ownership and decision authority
  Defined scope of responsibility
  Access to equivalent processing environment
  Agreement on required vs historical steps
  Clarity on PEDA expectations and support
  A concrete transition plan

## Slide 17: Automation in Parallel
Automation Approach
  Replicate existing assumptions first
  Validate automated outputs against current results
  Run side-by-side until equivalence is clear
  Make changes incrementally
  Preserve current endpoints throughout
  Automation as risk reduction, not behavior change

## Slide 18: Summary
Current process is well-understood and reliable
Transition requires clarity, not reinvention
Automation can proceed safely in parallel
Goal is continuity, stability, and gradual improvement